## Slide 1: Pipelining
By Paul Collado

## Slide 2: Parallelism
Two types of parallelism:
  Spatial parallelism
    duplicate hardware performs multiple tasks at once
  Temporal parallelism
    task is broken into multiple stages
    also called pipelining
    for example, an assembly line

## Slide 3: Parallelism Definitions
Some definitions:
  Token: A group of inputs processed to produce a group of outputs
  Latency: Time for one token to pass from start to end
  Throughput: The number of tokens that can be produced per unit time
Parallelism increases throughput
  Often sacrificing latency

## Slide 4: Parallelism Example
Ben is baking cookies
  It takes 5 minutes to roll the cookies and 15 minutes to bake them.
  After finishing one batch he immediately starts the next batch. What is the latency and throughput if Ben doesn’t use parallelism?
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 tray/ 1/3 hour = 3 trays/hour

## Slide 5: Parallelism Example
What is the latency and throughput if Ben uses parallelism?
  Spatial parallelism: Ben asks Allysa to help, using her own oven
  Temporal parallelism: Ben breaks the task into two stages: roll and baking. He uses two trays. While the first batch is baking he rolls the second batch, and so on.

## Slide 6: Spatial Parallelism
Latency = ?
Throughput = ?

## Slide 7: Spatial Parallelism
Latency = 5 + 15 = 20 minutes = 1/3 hour (same)
Throughput = 2 trays/ 1/3 hour = 6 trays/hour (doubled)

## Slide 8: Temporal Parallelism
Latency = ?
Throughput = ?

## Slide 9: Temporal Parallelism
Latency = 5 + 15 = 20 minutes = 1/3 hour
Throughput = 1 trays/ 1/4 hour = 4 trays/hour
Using both techniques, the throughput would be 8 trays/hour

## Slide 10: Ideal Pipeline Performance
If stages are perfectly balanced:
The more stages the better?
  Each stage typically corresponds to a clock cycle
  Stages will not be perfectly balanced
  Synchronous: Slowest stage will dominate time
  Many hazards await us
Two ways to view pipelining
  Reduced CPI (when going from non-piped to pipelined)
  Reduced Cycle Time (when increasing pipeline depth)

## Slide 11: Pipeline Concept
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 12: Traditional Pipeline Concept
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 13: Pipeline Concept
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 14: Pipeline Concept
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
Stall for Dependences
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 15: MIPS Without Pipelining
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D

## Slide 16: MIPS Functions
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Instruction Fetch (IF):
Send out the PC and fetch the instruction from memory into the instruction register (IR); increment the PC by 4 to address the next sequential instruction.
IR holds the instruction that will be used in the next stage.
NPC holds the value of the next PC.
Passed To Next Stage
IR <- Mem[PC]
NPC <- PC + 4

## Slide 17: MIPS Functions
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Instruction Decode/Register Fetch Cycle (ID):
Decode the instruction and access the register file to read the registers.
The outputs of the general purpose registers are read into two temporary registers (A & B) for use in later clock cycles.
We extend the sign of the lower 16 bits of the Instruction Register.
Passed To Next Stage
A <- Regs[IR6..IR10];
B <- Regs[IR10..IR15];
Imm <- ((IR16) ##IR16-31

## Slide 18: MIPS Functions
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
A <- A func. B
cond = 0;
Execute Address Calculation (EX):
We perform an operation (for an ALU) or an address calculation (if it’s a load or a Branch).
If an ALU, actually do the operation. If an address calculation, figure out how to obtain the address and stash away the location of that address for the next cycle.

## Slide 19: MIPS Functions
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
A = Mem[prev. B]
or
Mem[prev. B] = A
MEMORY ACCESS (MEM):
If this is an ALU, do nothing.
If a load or store, then access memory.

## Slide 20: MIPS Functions
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
IR
L
M
D
Passed To Next Stage
Regs <- A, B;
WRITE BACK (WB):
Update the registers from either the ALU or from the data loaded.

## Slide 21: The Basic Pipeline For MIPS
Latches between each stage provide pipelining.

## Slide 22: The Basic Pipeline For MIPS
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
I
n
s
t
r.
O
r
d
e
r

## Slide 23: Pipeline Hazards
Data Hazards – an instruction uses the result of the previous instruction. A hazard occurs exactly when an instruction tries to read a register in its ID stage that an earlier instruction intends to write in its WB stage.
Control Hazards – the location of an instruction depends on previous instruction
Structural Hazards – two instructions need to access the same resource

## Slide 24: Data Hazards

## Slide 25: Stalling
Stalling involves halting the flow of instructions until the required result is ready to be used. However stalling wastes processor time by doing nothing while waiting for the result.

## Slide 27: Summary
Pipelining attempts to use hardware more efficiently
Throughput increases at cost of latency
Hazards ensue
Modern processors pipelined